DAC200 / HA200 - Firmware update

Introduction
The recommended and safest way to update the firmware of a T+A DAC200 or HA200 is to use the T+A MP200 streamer. The MP200 will download the latest firmware and update the DAC/HA 200 over the T+A E2_Link.

T+A also provides an official and approved USB→E2_Link programming adapter and a programming tool for Windows PCs to allow a firmware update without the use of a MP200.

Non-official DIY update
If neither a MP200 nor a T+A programming adapter is at hand, the firmware update can also be done with a DIY „home-brew“ programming adapter consisting of a USB→RS232 converter, a RS232→TTL level converter and a short piece of Ethernet cable with RJ45 (T568B) plug.

Important note: This “DIY” update is not approved by T+A and it will be at your own risk !

For the update the T+A E2Link interface on the back panel of the DAC/HA devices is used.
The E2_Link uses a T+A proprietary serial protocol – this protocol is not standard RS232.

The method described in this document uses a standard USB→RS232 converter and a special programming software which mimics the T+A E-Link bus protocol. Because the timing of the serial communication is very critical, not all USB→RS232 converters on the market are suited.

Programming Adapter (DIY version)

My programming adapter consists of a plugable USB→RS232 adapter with prolific pl2303 chip set and a LC STUDIO RS232→TTL level converter.

DIY
USB→E_Link programming adapter

Wire connections to RJ45 cable

100 Ohm series resistors in TX and RX wires

RJ45 (T568B) E2-Link connections

1	orange/white	NC
2	orange	NC
3	green/white	RS232 – RX	(*)
4	blue	VCC (+5V)
5	blue/white	RS232 – TX	(*)
6	green	GND
7	brown/white	NC
8	brown	NC

(*) It is recommended to use protective 100 Ohm series resistors in the RX and TX lines (see picture above).

The +5V VCC voltage for the RS232→ TTL level converter is delivered from the T+A device via pin4 of the E2_Link.

Notes:
(1) In stead of a USB→RS232 plus RS232→TTL adapter a direct USB→5V RS232 adapter might be used.

(2) The firmware update was tested with a Prolific PL2303 USB→RS232 adapter.

(3) Please make sure to use only adapters with an original Prolific chip set – there are quite a few (very cheap) adapters with non-original Chinese fake Prolific chips on the market: These non original Prolific chip sets will probably not work properly in this application !

(4) FTDI FT232R based USB→RS232 converters will also work, but the latency for these chips must be set to 1ms.
The latency for FTDI chips can be set in the Windows device manager:
Device_Manager -> Ports(COM&LPT) -> USB_Serial_Port (COMx) -> Port Settings -> Advanced -> Latency_Timer
Programming Procedure

1. Start your Windows PC
2. Connect the programming Adapter to your PC and to the E2Link socket of the DAC/HA200
3. Switch ON your T+A device
4. For FTDI based USB→RS232 adapters: set the latency in Windows device manager to 1ms
5. Start the T+A E_Link Update Tool on your PC
6. Click on the „Select COM Port“ button (see picture below)
  - A drop-Down list will occur.
1. In the drop down list, select the COM port your programming adapter is connected to
2. Click on the button „Select Device“
3. From the drop-down list select the type of device you want to update (DAC200 or HA200)
4. Click on the connect button
  - The T+A update tool will now check the communication with the device and check if the connected device matches with the selected device type.
  - If you get any ERRORS at this stage, please check the cabling, the USB-ES232 adapter and the settings
  - If you get the response „Success: all pre-checks completed. We are ready to start update“, click on the „Update“button.
A file-selection window will open that permits to select the file with the new firmware.
  - Please note: The name of firmware update file must begin with „UPD_DAC_200“or „UPD_HA_200“
1. Select the firmware file by double-clicking on it
2. A „Start flash“ pop-up window will occur.
  - Press „Yes“ to start the update process or click on „No“ to cancel the update.
  - Note: this is the last chance to stop the update procedure. If you press „Yes“, the program memory in your T+A device will be erased and re-programmed.
Wait until the update process is finished.
  - The update process will last a couple of minutes.
  - Please be patient, do not disturb the programming, do not switch OFF the T+A device, do not remove any cables!
  - You will be informed about the upgrade progress by a couple of messages on the PC screen and by a progress-bar in the lower left corner of the program window.
After successful update, a pop-up window with the message „Update done“ will appear.
  - Click on „OK“ and restart your T+A device by pressing the Power button on the front panel of the DAC/HA_200.
If you get a „Programming ERROR“ pop-up message, something went wrong.
  - By clicking on the „Yes“ button in this pop-up window you can re-start the update process

After program start:
select COM port.

Pre-Checks done,
Ready to start update

Update finished successfully

Device recovery

If during programming a severe fault occurred (like eg. a mains power interruption during programming or unplugging of the programming cable), the T+A device will be left with an erased or non functional program memory. In this case the T+A device will not work any more but it can be recovered with the help of the T+A Update Tool.

For recovery please proceed as follows:

1. Disconnect the T+A device from the mains
2. Leave it disconnected for about 2 minutes
3. Re-connect the mains
4. Start your Windows PC
5. Connect the programming Adapter to your PC and to the E2Link socket of the DAC/HA200
6. For FTDI based USB→RS232 adapters set the latency in Windows device manager to 1ms
7. Start the T+A E_Link Update tool
  - The update tool will show the information that it has discovered a T+A device in Recovery Mode
1. Select „Recover“
2. Select the file with the device firmware
3. In the „Start Flash“ pop-up window select „Yes“
4. Wait until the program flash process has terminated.
5. After successful device recovery, a pop-up window with the message „Update done“ will appear.
  - Click on „OK“ and restart your T+A device by pressing the POWER button on the front panel of the DAC/HA_200.

Update Tool after	discovery of a T+A	device in recovery	mode